   Student Name 1: Curtis Collins
   Student Name 2: Lee-Ong Sim
   IP Address block: 172.20.__8__.__0____

Topology Diagram

Figure 1. Cabling the Network
## Task 1: Design the Logical Network.
Step 1-4: Design SubnetD address block.
Q1-Q4
Sub Network	Network Address	x.x.x.x Mask	/nn Mask	First Host Address	Last Host Address	Broadcast
D	172.20.8.0	255.255.255.128	/25	172.20.8.1	172.20.8.126	172.20.8.127
C	172.20.8.128	255.255.255.192	/26	172.20.8.129	172.20.8.190	172.20.8.191
B	172.20.8.192	255.255.255.248	/29	172.20.8.193	172.20.8.198	172.20.8.199
A	172.20.8.200	255.255.255.252	/30	172.20.8.201	172.20.8.202	172.20.8.203

Task 2: Configure the Physical Lab Topology.
Step 2: Network connections.

Q5 Host1 MAC Address : 00:01:64:E6:E0:89

Q6-Q11
From	To	Cable Type
Host_1	Router_1 Fa0/0	Crossover
Router_1 Fa0/1	Switch_1	Straight-Through
Host2	Switch_1	Straight-Through
Host3	Switch_1	Straight-Through

Task 3: Configure the Logical Topology.
Step 1: Document logical network settings.
Q12
Host1 (use first address from subnet A)
IP Address	172.20.8.201
IP Mask	255.255.255.252
Gateway Address	172.20.8.202
Host2 (use first address from subnet B)
IP Address	172.20.8.193
IP Mask	255.255.255.248
Gateway Address	172.20.8.198
Host3 (use second address from subnet B)
IP Address	172.20.8.194
IP Mask	255.255.255.248
Gateway Address	172.20.8.198
Router1 Interface Fa0/0
IP Address	172.20.8.202
IP Mask	255.255.255.252
Router1 Interface Fa0/1
IP Address	172.20.8.198
IP Mask	255.255.255.248

Task 4: Verify Network Connectivity.
Q13 [2 marks]
From	To	Source IP	Target IP	Ping Results
Host1	Gateway (Router1, Fa0/0)	172.20.8.201	172.20.8.202	Success
Host1	Router1, Fa0/1	172.20.8.201	172.20.8.198	Success
Host1	Host2	172.20.8.201	172.20.8.193	Success
Host1	Host3	172.20.8.201	172.20.8.194	Success
Host2	Host3	172.20.8.193	172.20.8.194	Success
Host2	Gateway (Router1, Fa0/1)	172.20.8.193	172.20.8.198	Success
Host2	Router1, Fa0/0	172.20.8.193	172.20.8.202	Success
Host2	Host1	172.20.8.193	172.20.8.201	Success
Host3	Host2	172.20.8.194	172.20.8.193	Success
Host3	Gateway (Router1, Fa0/1)	172.20.8.194	172.20.8.198	Success
Host3	Router1, Fa0/0	172.20.8.194	172.20.8.202	Success
Host3	Host1	172.20.8.194	172.20.8.201	Success

Q14 In the above scenario, how can a malfunctioning Gateway be detected?
You can find out if the gateway is malfunctioning by pinging it. If the ping is successful, the problem lies elsewhere. If the ping times out, then there is a malfunction along the PATH to the gateway, or in the gateway itself.
Task 6: Challenge [3 BONUS marks]
Ask your instructor to introduce one or two problems in your network , then fix them.
Perform a good visual inspection. Look at the status of the device ports by hovering your mouse over the device icon.

Use the table provided in Task 3 to identify failed connectivity. List the problems:
The first problem encountered was that the wrong cable was used to connect Host 1 to Router1.
The second problem we encountered was that the ip addresses for Interface 0/0 and 1/0 on	Router1 were switched.
Write down your proposed solution(s):
We propose to switch the current straight-through cable connecting Host1 and Router1 with a crossover cable instead. We will then proceed to revert the IP addresses for interfaces 0/0 and 1/0 on Router1, back to their original addresses of 172.20.8.202 (0/0) and 172.20.8.198 (1/0)
Test your solution. If the solution fixed the problem, document the solution. If the solution did not fix the problem, continue troubleshooting.
Our proposed solution worked just fine and dandy, flawless even, and thus we shall continue to dominate the networking world.

Note: At this point you should call your lab instructor to have your lab check in.

To be filled in by Lab Instructor

      ☺ IP subnetting ☺ Connectivity
      ☺ Cabling ☺ Problem / Fix

        Lab Instructor Mr. Anderson